OLPC  Test Plan and Process

Quanta Computer Inc.

1. Operation Flow Chart

A: OLPC Test Process

SMT  Test items:

check usb port

check bios version

camera

video memory

motherboard

CPU register check

SD

Battery temperature

Ambit temperature

NAND

USB 2.0

Wireless

LED

Touchpad

Display

Audio

Gamepad

Battery charge current

Set time to CMOS

FAT ( Final Ass’y Test):

check usb port

check cmos battery

check touch pad id

check battery

check bios version

check LED

input SN

get information from SF

write tags

copy test image

FRT ( Final Run In Test):

wireless

reboot

loop begin

memory

check battery

CPU burning

LCD burning

NAND

Battery temperature

Ambit temperature

loop end

FFT ( Final Function Test):

check routing

check bios version

check model

check sd

check camera

audio

check hardware configure

display

usb 2.0

touchpad

penwrite

gamepad

check battery temperature

check ambit temperature

check battery discharge current

keyboard

lid switch

IMG Down Load:

check AC

check hardware configure

check tags from SF

NTP

check battery capacity

copy shipping image

write tags

upload log to SF

System function Test Coverage and fixtures

| Coverage Item | Program/command | Fixtures | Location |
| --- | --- | --- | --- |
| LCD display and interface | OLPC-CL1 diag | LCD display LCD FPC | Function |
| Internal Keyboard and interface | OLPC-CL1 diag | Keyboard | Function |
| CPU and thermal cooler test | OLPC-CL1 diag | CPU and cooler | Run-in |
| Memory size and integrity test | OLPC-CL1 diag | 128MB module | Run-in |
| Touchpad and buttons test | OLPC-CL1 diag | Touchpad/Palmrest | Function (FQA) |
| Internet | OLPC-CL1 diag | Upper board | Function (FQA) |
| AC in detection | OLPC-CL1 diag | AC Adapter | Function & Run-in |
| Battery charge/discharge | BIOS Setup | Battery 12W | Function |
| RTC Backup battery | Manual Suspend/resume by battery plug/inout w/o AC power | N/A | Function |
| USB connector and interface test | OLPC-CL1 diag | USB flash drive | Function |
| Antenna test | OLPC-CL1 diag | Access point | Run-in& Function |
| S-Video cable and connector | OLPC-CL1 diag | LCD panel | Function (FQA) |
| Nand flash(Write, Reader, Paint, E-book, Block game, E-toy) | OLPC-CL1 diag | Nand flash | Function (FQA) |
| Battery charge LED | OLPC-CL1 diag | Battery (not full charged) | Function |
| Power LED | Visual | AC power or battery | Function |
| Internal speakers connectors and audio function | OLPC-CL1 diag | Internal/External speakers | Function |
| External microphone, speaker and connectors and audio function | OLPC-CL1 diag | MIC and active speaker | Function |
| External Mini DIN (keyboard signals) | N/A | External keyboard | Function |
| BIOS Re-flash | BIOS utility | None | Run-in |